## Slide 1: IoT Security and Privacy
Input/Output of ESP32
Xinwen Fu

## Slide 2: Outline
General-Purpose Input/Output (GPIO)
Universal Asynchronous Receiver/Transmitter (UART)
Inter-integrated circuit (I2C)
Serial Peripheral Interface (SPI)

## Slide 3: UART - I2C – SPI Serial communications

## Slide 4: ESP32-WROOM-32 Pin Layout
Notes: Type P: Power
Type I: Only for Input?
Type I/O: Input or output

## Slide 5: Schematic of Our Board

## Slide 6: Pins
Power pins
Input (only) pins
I/O pins
  GPIO (General-Purpose Input/Ooutput)
  May be used for special purposes
Pins SCK/CLK, SDO/SD0, SDI/SD1, SHD/SD2, SWP/SD3 and SCS/CMD, namely, GPIO6 to GPIO11 are connected to the integrated SPI flash integrated on the module and are not recommended for other uses.

## Slide 7: GPIO (General-Purpose Input/Ooutput)
These pins are a physical interface between a MCU and the outside world.
At the simplest level, you can think of them as switches that you can turn on or off (input) or that the MCU can turn on or off (output).

## Slide 8: Use of GPIO Pins
You can program the pins to interact in amazing ways with the real world.
It could be input from a sensor or a signal from another computer or device, for example.
The output can also do anything, from turning on an LED to sending a signal or data to another device.
If the IoT kit is on a network, you can control devices that are attached to it from anywhere** and those devices can send data back.
Connectivity and control of physical devices over the internet is a powerful and exciting thing, and the Raspberry Pi is ideal for this.

## Slide 9: Warning
If you follow the instructions, then messing about with the GPIO is safe and fun.
  Randomly plugging wires and power sources into your Pi, however, may kill it.
Bad things can also happen if you try to connect things to your board that use a lot of power; LEDs are fine, motors are not.
If you are worried about this, then you might want to consider using a breakout board such as the Pibrella until you are confident enough to use the GPIO directly.

## Slide 10: Output
GPIO outputs are on or off, HIGH or LOW, 3v3 or 0v.
When we use a GPIO pin as an output as shown in the right diagram, the IoT kit replaces both the switch and the battery in the left diagram.
  Each pin can turn on or off, or go HIGH or LOW in computing terms. When the pin is HIGH it outputs 3.3 volts (3v3); when the pin is LOW it is off.

## Slide 11: LED (Light-Emitting Diode)
LED is polarized
Many identifiers for finding positive and negative pins
  E.g. longer leg should indicate the positive, anode pin.

## Slide 12: Resistor
The gold/silver band shall be held on the right

## Slide 13: INPUT
Inputs are a bit trickier because of the way that digital devices work.
You will see phrases like "pull up" and "pull down" in GPIO tutorials.
  It's a way of giving the input pin a reference so it knows for certain when an input is received.

## Slide 14: Other Use of GPIO pins
UART (Universal Asynchronous Receiver/Transmitter)
SPI (Serial Peripheral Interface)
I2C (Inter-integrated circuit)
PWM (pulse-width modulation)

## Slide 15: Outline
General-Purpose Input/Output (GPIO)
Universal Asynchronous Receiver/Transmitter (UART)
Inter-integrated circuit (I2C)
Serial Peripheral Interface (SPI)

## Slide 16: Serial vs Parallel

## Slide 17: Synchronous vs. Asynchronous
Synchronous data transfer: sender and receiver use the same clock signal
  supports high data transfer rate
  needs clock signal between the sender and the receiver
  requires master/slave configuration
Asynchronous data transfer: sender provides a synchronization signal to the receiver before starting the transfer of each message
  does not need clock signal between sender the receiver
  slower data transfer rate

## Slide 18: UART (Universal Asynchronous Receiver/Transmitter)
Hardware translates between parallel and serial forms
  Takes bytes of data and transmits the individual bits in a sequential fashion.
  At the destination, a second UART re-assembles the bits into complete bytes.
Commonly used in conjunction with communication standards such as EIA, RS-232, RS-422 or RS-485
The universal designation indicates that
  Data format and transmission speeds are configurable

## Slide 19: Tx and Rx
The UART has a transmission engine, and also a reception engine
  They can operate simultaneously
Software controls the UART’s operations by accessing several registers, using the CPU’s input and output instructions

## Slide 20: Serial Data Transmission
Software outputs a byte of data to the THR
The bits are immediately copied into an internal ‘shift’-register
The bits are shifted out, one-at-a-time, in sync with a clock-pulse
0
1
1
0
0
0
0
1
Transmitter Holding Register (8-bits)
0
1
1
0
0
0
0
1
transmitter’s internal ‘shift’ register
clock
1-0-1-1-0-0-0-0-1-0
start
bit
stop
bit
data-bits
clock-pulses
trigger bit-shifts
❶
❷
❸

## Slide 21: Serial data reception
clock
input voltage
clock-pulses trigger voltage-sampling and bit-shifts at regular intervals
0
1
1
0
0
0
0
1
Receiver’s internal ‘shift’ register
1-0-1-1-0-0-0-0-1-0
start
bit
stop
bit
data-bits
0
1
1
0
0
0
0
1
Receiver Buffer Register (8-bits)
Software can retrieve the received byte from the RBR

## Slide 22: Outline
General-Purpose Input/Output (GPIO)
Universal Asynchronous Receiver/Transmitter (UART)
Inter-integrated circuit (I2C)
Serial Peripheral Interface (SPI)

## Slide 23: I2C (I2C, IIC, Inter-integrated circuit)
Pronounced “eye-squared-see”
Two-wire serial bus protocol
  Between MCUs and sensors
  Speed up to 3.4Mbits/s
Invented by Philips in the early 1980’s
  The division now spun off into NXP

## Slide 24: I2C Advantages and Disadvantages
Advantages
  Needs two signal connections to MCU
  Allows multiple devices on the two connections
  Gets acknowledgment that signals have been correctly received
Disadvantages
  Data rate is slower than SPI (Serial Peripheral Interface)
  Data can only be traveling in one direction at a time, lowering the data rate even more if two-way communication is needed.
  Necessary to connect pull-up resistors to the connections to ensure reliable transmission of signals

## Slide 25: Two Connections
The two connections for the I2C bus are called
  SCL (clock) and
  SDA (data).
One device on the I2C bus is considered the master device.
  Coordinate the transfer of information between the other devices (slaves) that are attached.
  There must be only one master like the MCU

## Slide 26: Slave Devices
Slave devices are identified by their address number
Each slave must have a unique address.
  Some I2C devices have a fixed address
  while others allow you to configure their address by setting pins high or low or by sending initialization commands

## Slide 27: Outline
General-Purpose Input/Output (GPIO)
Universal Asynchronous Receiver/Transmitter (UART)
Inter-integrated circuit (I2C)
Serial Peripheral Interface (SPI)

## Slide 28: SPI (Serial Peripheral Interface)
A synchronous circuit is a digital circuit in which the changes in the state of memory elements are synchronized by a clock signal
  SCLK (SCK): Serial Clock (output from master)
  MOSI: Master Out Slave In (data output from master)
  MISO: Master In Slave Out (data output from slave)
  SS (CS): Slave Select (often active low, output from master)

## Slide 29: Advantages of SPI
it runs at a higher data rate, and
it has separate input and output connections, so it can send and receive at the same time
  Duplex
It uses one additional line per device to select the active device, so more connections are required if you have many devices to connect.

## Slide 30: Comparison

## Slide 31: Uplayer Protocol
UART, I2C and SPI only define how communication takes place between devices
The messages that need to be sent depend on each individual device and what it does.
You will need to consult the data sheet for your device to determine what commands are required to get it to function, and what data is required, or returned.

## Slide 32: References
[1] GPIO, Accessed on Feb. 25, 2021
[2] I2C, Accessed on Feb. 25, 2021
[3] SPI, Accessed on Feb. 25, 2021