## Slide 1: IoT Security and Privacy
ARM TrustZone

## Slide 2: Learning Outcomes
Upon completion of this unit:
Students will understand the system security
Students will understand TrustZone hardware architecture
Students will understand TrustZone software architectures

## Slide 3: Outline
Introduction
System security
TrustZone Hardware Architecture
TrustZone Software Architecture
TrustZone System Design

## Slide 4: What is security?
Asset – A worth protecting resource of value
  Tangible object (?), such as a user password
  Intangible asset, such as network availability
To Attack
  Intentional act of acquisition, damage or disruption of an asset without permission
  Attack tools: software, hardware monitoring and hardware tampering
To Defend
  Design of a system with hardware or software to counter attacks.

## Slide 5: Threats against Market sector-Mobile sector
The International Mobile Equipment Identity (IMEI) code
  Identify a handset
  Block a stolen one using the cellular network, when reported
Low level SIMLock protocol
  Bind a handset to a SIM from a service operator during the contract
Can be bypassed through a USB cable and a reprogramming tool running on a desktop
  Industry losing big money because of this
  E.g., selling illegally unlocked phones with a discount price from a phone company
Data on mobile devices needs security
  digital Rights Management (DRM)
  confidential user data like synchronized email accounts?

## Slide 6: Threats against Market sector - Consumer electronics and embedded sector
Consumer electronics
Embedded sector
Odometer fraud – rollback of odometer of a second-hand vehicle

## Slide 7: Class-breaking attacks
Who are the attackers?
  professional criminals ( for financial gain)
  academic security researchers (for academic prestige), and
  enthusiasts working at home (for fun)
Most sought achievement - class-break: attacks that break a whole generation, or class, of devices.
  Consumer entertainment devices: software restrictions on games consoles and the content protection schemes on DVD movies
Invest for class break attacks
  Initial investment could be big such as electron microscopes and transistor stimulating lasers for silicon-level analysis

## Slide 8: How are devices attacked?
Hack attack – software attack by hackers
  Viruses and malware
  Why possible? One reason: “Given a choice between dancing pigs and security, users will pick dancing pigs every time.” 
Shack attack - low-budget hardware attack from cheap off-the-shelf tools bough from for example Radio Shack
  Hardware interface attack, not attack against integrated circuit packages.
  Examples: JTAG debug, boundary scan I/O, and built-in self test facilities.
  Attacks: forcing pins and bus lines to be at a high or low voltage, reprogramming memory devices, and replacing hardware components with malicious alternatives.

## Slide 9: How are devices attacked? (Cont’d)
Lab attack – unlimited reverse engineering with sophisticated equipment such as electron microscopes
  Most comprehensive and invasive
  Rule of thumb: every device can be broken
  We can make the lab attack uneconomic – for example, Use of per-device unique secrets, so that the attack is limited to one compromised device

## Slide 10: Who attacks devices?
Lab attacks are outside of the scope of the protection provided TrustZone technology
Remote attacker
  Increased complex software on embedded devices
  Installation of code from the Internet
Security specialist
  “The most technically capable attackers are criminal gangs, security experts, and users attacking devices for fun.”
“Trusted” developer – insider attack
  Can be mitigated by defensive measures in business process
Device owner
  Gaining free access to services and content.
  Often script kiddies using approaches from the Internet
  Exposed to embedded malware

## Slide 11: Security features for these embedded systems
Secure firmware updates
Secure debug mechanisms
Can be implemented with TrustZone

## Slide 12: Risk analysis
Risk analysis
  Probability of a successful attack,
  Cost to the business for a successful attack
  Cost of defense
Example risk analysis outcomes
  Probability of an attack too low to be worth defending
  Cost of a defense too high for the asset of interest
  Justified asset defense
TrustZone is cost efficient for various asset defense
“Professional hackers are predominantly motivated by financial gain.”

## Slide 13: Positive Economics
A good payment system stimulates spending by 20%
  Easy to use
  Secure
  Increased consumer confidence
  New revenue streams
  Different business models.
Security features differentiate manufacturers

## Slide 14: Limitations of security solutions
We can only counter a subset of possible attacks
  Impossible to counter all possible attacks
A security design must identify
  what assets to protect
  what attacks to counter
If an attack needs too much money and time
  The defense is a success
  The attacker most possibly will move on to next target!!!

## Slide 15: Hardware enforced security
Trusted Computing Group recommends
  Dedicated hardware from the start of system design
  Processor-level, SoC infrastructure based
ARM TrustZone
  Uses ARM processor, bus fabric, and system peripheral IP
  Provides a framework to support flexible secure system architectures without adding much cost
System on a chip

## Slide 16: Components of SoC
A microcontroller, microprocessor or digital signal processor (DSP) core – multiprocessor SoCs (MPSoC)
Memory blocks including ROM, RAM, EEPROM and flash memory
Timing sources including oscillators and phase-locked loops
Peripherals including counter-timers, real-time timers and power-on reset generators
External interfaces, including industry standards such as USB, FireWire, Ethernet, USART, SPI analog interfaces including ADCs and DACs
Voltage regulators and power management circuits
A bus connecting these blocks.
DMA controllers routing data directly between external interfaces and memory, bypassing the processor core and thereby increasing the data throughput of the SoC.
https://en.wikipedia.org/wiki/System_on_a_chip

## Slide 17: Outline
Introduction
System security
TrustZone Hardware Architecture
TrustZone Software Architecture
TrustZone System Design

## Slide 18: Embedded Device Design
Functional components (for the target application)
  Multiple independent processor cores
  Secondary bus masters such as DMA engines
  large numbers of memory
  Peripheral bus slaves
Non-function components
  Invasive and non-invasive debug capabilities
  Component boundary scan: a method for testing interconnects of a board
  Built-In-Self-Test (BIST) facilities
Security solution has to address all above

## Slide 19: System security strategy - External hardware security module
A dedicated hardware security module, or trusted element, outside of the main SoC
  A SIM card in a mobile handset
  A conditional access smartcard in a set-top box.
Advantages
  Work well for the assets it protects
Disadvantage of external hardware security module (e.g. smartcard)
  Cannot protect assets outside of the external hardware, e.g. pin/password

## Slide 20: Internal hardware security module
Two main forms
  Hardware block which manages cryptographic operations and key storage
  General purpose processing engine placed alongside the main processor
Advantages
  Cost effective compared to the use of many smartcards for different assets
Disadvantages
  Cryptographic hardware block has similar issues like smartcard
  A second security processor introduces complexities such as communication between the main processor and itself

## Slide 21: Software virtualization
A hypervisor
  Uses the Memory Management Unit (MMU)
  Runs independent software platforms inside a virtual machine
Advantages
  Flexible
Disadvantages
  The isolation is restricted to the processor implementing the hypervisor.
  Other bus masters such as DMA and GPUs can bypass the protection

## Slide 22: TrustZone hardware security
Protection strategies discussed so far are dedicated to specific assets
TrustZone is for system-wide security
  Protects any part of the system
  Can be used with other security strategies such as secure boot, authenticated debug mode and unique secret for each device

## Slide 23: Outline
Introduction
System security
TrustZone Hardware Architecture
TrustZone Software Architecture
TrustZone System Design

## Slide 24: TrustZone Hardware Architecture
It constructs a programmable environment that protects almost any asset
Any SoC hardware and software resources exist in two worlds
  Secure world
  Normal ( Non-secure) world
Hardware logic in the TrustZone-enabled AMBA3 AXI™ bus fabric ensures
  normal world components cannot access secure world resources
A single ARM core of some version can execute code from both normal world and secure world in a time sliced fashion
  No need of dedicated secure processor
It has a security-aware debug infrastructure that limits Secure world debug

## Slide 25: System architecture
The AMBA3 AXI system bus
  An extra control signal, Non-Secure, or NS bits, for each of the read and write channels on the main system bus.
The AMBA3 APB peripheral bus
  Secure peripherals, such as interrupt controllers, timers, and user I/O devices, for example, a securable keyboard peripheral that protects a user password.
  Use of Advanced Peripheral Bus (APB) attached to the system bus through an AXI-to-APB bridge
Memory aliasing
  The NS bit is equivalent to a 33rd address bit, a 32-bit physical address space for Secure transactions and a 32-bit physical address space for Non-secure transactions
  The same memory location appears as two distinct locations in Secure and Non-secure worlds – needs to be taken care

## Slide 26: Processor architecture
ARM processors with security extensions
  ARM1176JZ(F)-S™ processor
  Cortex™-A8 processor
  Cortex-A9 processor
  Cortex-A9 MPCore™ processor
Normal world
Normal world user mode
Normal world privileged modes
Secure world
Secure world user mode
Secure world privileged modes
Monitor mode
[1]
Each physical processor core has two virtual cores
  Secure
  Non-secure
  Monitor mode as context switch

## Slide 27: Switching worlds
Monitor mode – a new core mode
Tightly controlled switching mechanisms
  Viewed as exceptions to the monitor mode software
  can be triggered by the Secure Monitor Call (SMC) instruction by a subset of the hardware exception mechanisms
The monitor mode software is implementation defined
  Saves the state of the current world and
  restores the state of the world being switched to
  Performs a return-from-exception to restart processing in the restored world.
NS-bit in the Secure Configuration Register (SCR) in CP15 (the system control coprocessor) indicates the world of the processor
  In monitor mode, the processor executes in the Secure world

## Slide 28: Outline
Introduction
System security
TrustZone Hardware Architecture
TrustZone Software Architecture
TrustZone System Design

## Slide 29: TrustZone Software Architecture
The Security Extensions are an open component of the ARM architecture
Any developer can create a custom Secure world software environment to meet their requirements.

## Slide 30: Software architecture
The most complex is a dedicated Secure world operating system
The simplest is a synchronous library of code placed in the Secure world
Many options between the most complex and the simplest

## Slide 31: Software architecture (Cont’d)
Secure operating system
  Can simulate concurrent execution of multiple independent Secure world applications
  run-time download of new security applications
  Secure world tasks completely independent of the Normal world environment.
Synchronous library
  Handle one task at a time is sufficient for many applications

## Slide 32: Booting a secure system [1]
Device power on
ROM SoC Bootloader
(First Level Boot)
Flash Device Bootloader
(Second Level Boot)
Secure World OS Boot
Normal World Bootloader
Normal World OS Boot
System Running

## Slide 33: Secure boot
A trusted vendor
  Uses their Private Key (PrK) to sign the code of interest
  pushes this to the device alongside the software binary.
The device contains the Public Key (PuK) of the vendor,
  Verify that the binary has not been modified and
  It was provided by the trusted vendor in question.
The PuK does not need to be kept confidential
  need to be stored within the device in a manner which means it cannot be replaced by a PuK that belongs to an attacker.

## Slide 34: Chain of trust
“Starting with an implicitly trusted component, every other component can be authenticated before being executed.”
A public key (PuK) belonging to the device OEM might be used to authenticate the first bootloader
  but the Secure world OS binary might include a secondary PuK that is used to authenticate the applications that it loads.
The root of trust must be located in the on-SoC ROM.
  The SoC ROM is the only component that cannot be trivially attacked.
Storage of the PuK for the root of trust is a challenge
  Embedding it in the on-SoC ROM?
  On-SoC One-Time-Programmable (OTP) hardware, such as poly-silicon fuses, can be used to store unique values in each SoC during device manufacture.
Notes:   Embedding it in the on-SoC ROM? implies that all devices use the same PuK.
  This makes them vulnerable to class-break attacks if the PrK is stolen or successfully reverse-engineered.
  This enables a number of different PuK values to be stored in a single class of devices, reducing risk of class break attacks.

## Slide 35: ESP32 Secure Boot (V1)
The options to enable secure boot are provided in the Project Configuration Menu, under “Secure Boot Configuration”.
Secure Boot defaults to signing images and partition table data during the build process
The “Secure boot private signing key” config item is a file path to a ECDSA public/private key pair in a PEM format file
  Secure boot signing key is a standard ECDSA public/private key pair
  The public key is compiled into the software bootloader
  The private key must be securely kept private
The software bootloader image is built by esp-idf with secure boot support enabled and the public key (signature verification) portion of the secure boot signing key compiled in.
  This software bootloader image is flashed at offset 0x1000.

## Slide 36: ESP32 Secure Boot - On first boot
Hardware secure boot support generates a device secure bootloader key (generated via hardware RNG, then stored read/write protected in efuse), and a secure digest
  The digest is derived from the key, an IV, and the bootloader image contents.
  The secure digest is flashed at offset 0x0 in the flash.
Bootloader permanently enables secure boot by burning the ABS_DONE_0 effuse
  the chip will only boot a bootloader image if the digest matches.

## Slide 37: ESP32 Secure Boot - Subsequent boots
The ROM bootloader sees that the secure boot efuse is burned,
  reads the saved digest at 0x0 and
  uses hardware secure boot support to compare it with a newly calculated digest.
  If the digest does not match then booting will not continue.
The digest and comparison are performed entirely by hardware, and the calculated digest is not readable by software.
When running in secure boot mode, the software bootloader uses the secure boot signing key (the public key of which is embedded in the bootloader itself, and therefore validated as part of the bootloader) to verify the signature appended to all subsequent partition tables and app images before they are booted.

## Slide 38: ESP32 Secure Boot – No OTA Illustration
Signature
factory app
0x010000
Signature
partition table
0x020000
phy_init
0x017000
nvs
0x011000
(public key of
secure boot signing key)
software bootloader
0x001000
secure digest
ROM
Reserved | Flash encryption key | Secure bootloader key | Reserved for application
BLK0
BLK1
BLK2
BLK3
0x000000
eFuse

## Slide 39: ESP32 Secure Boot – OTA Illustration
Signature by Secure Boot signing key
0x008000
Signature
Partition table
0x010000
Signature
factory app
0x00d000
otadata
phy_init
0x00f000
nvs
0x009000
Signature
ota_0
0x110000
Signature
ota_1
0x210000
(Public key of Secure Boot signing key)
second-stage bootloader
0x001000
Secure digest

## Slide 40: eFuse blocks
ESP32 has 4 eFuse blocks as secure key storage
  Each is 256 bits
Reserved | Flash encryption key | Secure bootloader key | Reserved for application
BLK0
BLK1
BLK2
BLK3
eFuse

## Slide 41: ESP32 Secure Boot (V2)
Secure Boot V2 verifies the signature blocks appended to the bootloader and application binaries.
  The signature block contains the image binary signed by an RSA-3072 private key and its corresponding public key.
On startup, ROM code checks the Secure Boot V2 bit in eFuse.
If secure boot is enabled, ROM checks the SHA-256 of the public key in the signature block in the eFuse.
The ROM code validates the public key embedded in the software bootloader’s signature block by matching the SHA-256 of its public key to the SHA-256 in eFuse as per the earlier step.
  Boot process will be aborted if a valid hash of the public key isn’t found in the eFuse.

## Slide 42: ESP32 Secure Boot (V2) – Signature verification
The ROM code verifies the signature of the bootloader with the pre-validated public key with the RSA-PSS Scheme.
Software bootloader, reads the app partition and performs similar verification on the application.
The application is verified on every boot up and OTA update.
If selected OTA app partition fails verification, bootloader will fall back and look for another correctly signed partition.

## Slide 43: ESP32 Secure Boot (V2) – Illustration
Bootloader
RSA SignatureBL
RSA public key
App
RSA SignatureApp
RSA public key
eFuse
SHA-256 of
RSA public key
ROM

## Slide 44: On-SoC Secure world or Off-SoC Secure world
The simplest defense against shack attacks is to keep any Secure world resource execution located in on-SoC memory locations.
  A physical attack on the SoC package is hard
The secure boot code is generally responsible for loading code into the on-SoC memory, how to authentication the code?
  Code or PuK to authenticate should be performed in secure world

## Slide 45: Monitor mode software
A gatekeeper that manages the switches between the Secure World and Non-secure World.
Like a traditional operating system context switch, “ensuring that
  state of the world that the processor is leaving is safely saved, and
  the state of the world the processor is switching to is correctly restored.”
  Critical component to ensure the TrustZone mechanism
Best practice: disable interrupts in the monitor mode
  Complex with enabled interrupts
  Benefit is not big

## Slide 46: The TrustZone API
ARM provides a standardized software API, called the TrustZone API (TZAPI)
  A software interface for client applications in the non-secure (rich) operating environment interact with the secure world.
TZAPI is mainly a communications API
  A client sends command requests to a security service
  The client exchanges data with the security services
  The interface support World-shared memory shared by both normal world and secure world, for high performance bulk data transfer.

## Slide 47: A System Using TrustZone API [1]
Normal world
Secure world
Client Application
TZAPI
TZAPI library
TZAPI driver
Secure service
Service API
Service library
Service manager
Monitor mode

## Slide 48: Outline
Introduction
System security
TrustZone Hardware Architecture
TrustZone Software Architecture
TrustZone System Design

## Slide 49: Gadget2008 product design brief
A portable cellular handset
Feature-rich operating system capable executing user downloaded applications.
Audio and video playback with DRM content protection
GadgetStore will allow the user to pay for downloaded content using standard banking facilities

## Slide 50: Content management
A Digital Rights Management (DRM) agent enforces the access to media content based on the purchased rights by the user
  expiry date, number of plays, number of minutes of playback, and the playing device
For a DRM protected file for playback,
  The agent must ensure that the user’s rights are still valid and,
  if they are, decrypt the file and pass it to the media player.

## Slide 51: Integration in a system using TrustZone technology
DRM agent component in the Secure world
  rights storage, rights validation and content decryption
CODEC and media player in the Normal world.
  What can be the problem?
CODEC stack in the Secure world?
  Too complicated to avoid bugs!
Notes: Although this exposes the decrypted content to a degree of risk, mechanisms such as
anti-virus can be used to detect unauthorized changes to the Normal world operating
system and the media player, at which point the Secure world can stop sending content
to the Normal world.

## Slide 52: Assets
Assets | Security | Description
Rights Data | Authenticity | the information about the user’s rights
Rights Checking Code | Authenticity | checks the rights object must be authentic and executed from a secure location
Device Key | Confidentiality, Integrity | the root secret that is used to decrypt the rights data when transmitted from the content store.
Content Key | Confidentiality | the secret key which is stored in a rights object, and is used to decrypt a specific piece of content before playback.
Content Data | Confidentiality | decrypted content that is passed to media player

## Slide 53: Attackers
Device owner who wants to enjoy more …
Attacks
  software hack attacks
  simple hardware attacks

## Slide 54: General specification - Secure boot
Secure boot code located in on-SoC ROM
256-bits of OTP fuse for a SHA256 hash of the RSA public key owned by the Secure world software developer
  Authenticate the public key when needed
  Then validate certificates of code on the device
A statistically unique secret key located in an on-SoC cryptographic accelerator.
  Available only to Secure software
  Not trivial to recover the secret key from SoC, so it is safe
  Confidential data can be encrypted and bound to the device.
  Used as the device key?
Notes: Secure boot code located in on-SoC ROM
256-bits of OTP fuse which can contain a SHA256 hash of the RSA public key owned by the Secure world software developer
  We can distribute devices with a variety of root keys, reducing the risk of a successful class break attack.
  For secure boot, validating the measurements?
A statistically unique secret key located in an on-SoC cryptographic accelerator.
  Confidential data can be encrypted and bound to the device.
  The only mechanism to recover the secret key is to perform side-channel analysis of the cryptography, which the hardware accelerator design should prevent, or to dismantle the silicon to recover the key.
  Used as the device key?

## Slide 55: General specification (Cont’d)
Multi-tasking Secure world software
  The Gadget2008 design – multiple pieces of software in the Secure world: a DRM agent, a secure GadgetStore shopping backend, and a payment application.
  A Secure world operating system using the MMU to separate user tasks.
Securing the debug channels
  Two batches of production devices.
  The initial batch with full debug access, including Secure world access, for use by only trusted parties, with the OTP fuse set to a known invalid key.
  The second batch of devices with enabled Normal world debug and permanently disabled all Secure world debug using a fuse.

## Slide 56: Content management specification
Software video decoding
Soft real-time performance
Non-volatile counter to defend against a replay attack
  An attacker replaces a file system image containing an expired rights object with an older version containing the rights object before it had expired
Secure real-time clock source
Memory requirements

## Slide 57: References
[1] ARM Security Technology Building a Secure System using TrustZone® Technology, 2009
[2] Secure the Windows 10 boot process, 06/23/2017