## Slide 1: IoT Security and Privacy
Flash Encryption
Xinwen Fu

## Slide 2: Outline
Introduction
Secure storage
Flash Encryption Process

## Slide 3: Overview
Flash encryption encrypts the ESP32’s off-chip flash memory
When it is enabled
  We flash plaintext firmware
  The data is encrypted on the first boot
  Dumping flash will not recover most flash contents
Secure Boot is a separate feature
  Secure boot and flash encryption can work together

## Slide 4: Encrypted Data by Flash Encryption
Data encrypted by default
  Firmware bootloader (second stage bootloader)
  Partition Table
  All “app” type partitions
Other types of data conditionally encrypted
  Secure Boot bootloader digest if Secure Boot is enabled
  Any partition marked with the encrypted flag in the partition table

## Slide 5: Development v.s. Release Mode
Development Mode
  recommended for use ONLY DURING DEVELOPMENT, as it does not prevent modification and readout of encrypted flash contents
Release Mode
  recommended for manufacturing and production to prevent physical readout of encrypted flash contents (?)
  For production use, flash encryption should be enabled in the “Release” mode only

## Slide 6: Warning
Enabling flash encryption limits the options for further updates of ESP32
  Before using this feature, read the document and make sure to understand the implications.
Development mode is ok with some complexities of updating ESP32
Release mode can be problematic with wrong operation

## Slide 7: Challenge
Where shall the flash encryption key be stored?
How shall the flash encryption key be protected against malicious Read/Write?

## Slide 8: eFuse in Flash Encryption
eFuse | Description | Bit Depth
CODING_SCHEME | Controls actual number of block1 bits used to derive final 256-bit AES key. Possible values: 0 for 256 bits, 1 for 192 bits, 2 for 128 bits. Final AES key is derived based on the FLASH_CRYPT_CONFIG value. | 2
flash_encryption (block1) | AES key storage. | 256 bit key block
FLASH_CRYPT_CONFIG | Controls the AES encryption process. | 4
DISABLE_DL_ENCRYPT | If set, disables flash encryption operation while running in Firmware Download mode. | 1
DISABLE_DL_DECRYPT | If set, disables flash decryption while running in UART Firmware Download mode. | 1
FLASH_CRYPT_CNT | Enables/disables encryption at boot time. If even number of bits set (0, 2, 4, 6) - encrypt flash at boot time. If odd number of bits set (1, 3, 5, 7) - do not encrypt flash at boot time. | 7

## Slide 9: Read/write access to eFuse bits
Use espefuse.py
  Two commands: read_protect_efuse and write_protect_efuse
  Example espefuse.py write_protect_efuse DISABLE_DL_ENCRYPT
R/W access control by software is available for all the eFuse bits listed in the table above.
  The default value of these bits is 0 afer manufacturing.

## Slide 10: Outline
Introduction
Secure storage
Flash Encryption Process

## Slide 11: Types of Secure Storage
One-time programmable memory
  eFuse in ESP32
Crypto processors
  TPM
  ATECC608

## Slide 12: One-time programmable memory
The ESP32 has a 1024-bit eFuse
eFuse is a one-time programmable memory
This eFUSE is divided into 4 blocks of 256-bits each.

## Slide 13: Trusted Platform Module (TPM)
TPM technology is designed to provide hardware-based, security-related functions.
A TPM chip is a secure crypto-processor that is designed to carry out cryptographic operations.
The chip includes multiple physical security mechanisms to make it tamper-resistant, and malicious software is unable to tamper with the security functions of the TPM.

## Slide 14: Advantages of using TPM
Generate, store, and limit the use of cryptographic keys.
Use TPM technology for platform device authentication by using the TPM’s unique RSA key, which is burned into it.
Help ensure platform integrity by taking and storing security measurements.

## Slide 15: TPM-Based Sealed Storage
Software on the platform’s main CPU seals or binds secrets to a set of measurements representing some future platform state
  Both operations (seal and bind) essentially encrypt the secret value provided by the software.
TPM will refuse to perform a decryption, unless the current values in its Platform Configuration Registers (PCR) match those specified during the seal or bind operation.

## Slide 16: Full disk encryption
The disk encryption keys can be sealed to measurements representing the user’s operating system (Specific OS, disk encryption keys)
  e.g. Microsoft BitLocker does it [2]
  The disk can only be decrypted if the intended OS kernel has booted?
Connecting disk encryption with code identity ensures that
  Boot sequence cannot be changed to load malware or other OS
Seal and bind operations use 2048-bit asymmetric RSA keys
  RSA keys are generated on TPM
  Private keys are never released in the clear.
  Encryption scheme provides both secrecy and integrity

## Slide 17: Simplified BitLocker boot process
TPM
BIOS/EFI
MBR/BOOT LOADER
Operating System
(Encrypted)
RAM
1.1: Read and hash
1.2: Save to PCRs
2.1: Unseal key after verification
1.3: Pass control
2.3: Pass control
2.2: Save key to RAM
3: Use key as needed
Data flow
Control flow
Legend
KTPM(h, kd)
h’
Notes: 1. The BIOS/EFI hashes the next boot stage: the MBR, bootloader, etc. It puts the result in TPM
PCRs. Control is passed to the next boot stage.
2. The Windows bootloader asks the TPM to unseal the BitLocker encryption key, which will verify
the current PCR values. The returned key is stored in RAM, the operating system is decrypted, and
control is passed to the operating system.
3. The operating system continues to decrypt disk contents on the y using the key stored in RAM.

## Slide 18: Outline
Introduction
Secure Key Storage
Flash Encryption Process

## Slide 19: Flash Encryption Process
Assuming
  The eFuse values are in their default states
  The firmware bootloader is compiled to support flash encryption

## Slide 20: Flash Encryption Process (Cont’d)
On the first power-on reset
  all data in flash is un-encrypted (plaintext)
  The ROM bootloader loads the firmware bootloader
Firmware bootloader
  Reads the FLASH_CRYPT_CNT eFuse value (0b0000000)
    Since FLASH_CRYPT_CNT==0 (even number of bits set), it configures and enables the flash encryption block which performs encryption
  Sets the FLASH_CRYPT_CONFIG eFuse to 0xF
  Generate an AES-256 bit key and then writes it into the flash_encryption eFuse
    The key is not accessible to software

## Slide 21: Flash Encryption Process (Cont’d)
Flash encryption block encrypts the flash contents
  Firmware bootloader, applications and partitions marked as encrypted
Firmware bootloader
  Sets the first available bit in FLASH_CRYPT_CNT (0b0000001) to mark the flash contents as encrypted (Odd number of bits is set)
  For Development Mode
    Firmware bootloader sets only eFuse bits DISABLE_DL_DECRYPT and DISABLE_DL_CACHE and allows the UART bootloader to re-flash encrypted binaries
    FLASH_CRYPT_CNT eFuse bits are NOT write-protected.
  For Release Mode
    Firmware bootloader sets the eFuse bits DISABLE_DL_ENCRYPT, DISABLE_DL_DECRYPT, and DISABLE_DL_CACHE to 1 to prevent the UART bootloader from decrypting the flash contents.
    It also write-protects the FLASH_CRYPT_CNT eFuse bits.

## Slide 22: Flash Encryption Process (Cont’d)
The device reboots to start executing the encrypted image
  The firmware bootloader calls the flash decryption block to decrypt the flash contents and
  then loads the decrypted contents into IRAM (Instruction RAM), which is part of the Internal SRAM region for instruction RAM

## Slide 23: Notes
Leaving DISABLE_DL_DECRYPT unset (0) makes flash encryption useless.
An attacker with physical access to the chip can use UART bootloader mode with custom stub code to read out the flash contents.

## Slide 24: Release Mode
In Release mode, UART bootloader cannot perform flash encryption operations
New plaintext images can ONLY be downloaded using the over-the-air (OTA) scheme
  which will encrypt the plaintext image before writing to flash

## Slide 25: Limitations of Flash Encryption
Flash encryption does not prevent an attacker from understanding the high-level layout of the flash
  This is because the same AES key is used for every pair of adjacent 16 byte AES blocks
  When these adjacent 16 byte blocks contain identical content (such as empty or padding areas), these blocks will encrypt to produce matching pairs of encrypted blocks
Flash encryption alone may not prevent an attacker from modifying the firmware of the device
  To prevent unauthorised firmware from running on the device, use flash encryption in combination with Secure Boot.

## Slide 26: JTAG Debugging
By default, when Flash Encryption is enabled (in either Development or Release mode) then JTAG debugging is disabled via eFuse
The bootloader does this on first boot, at the same time it enables flash encryption.