## Slide 1: IoT Security and Privacy
Overview of IoT

## Slide 2: Learning Outcomes
Upon completion of this unit:
Student will understand different visions of the Internet of Things (IoT) paradigm
Students will understand the enabling technologies, their advantages and disadvantages
Students will understand different aspects of IoT security and privacy

## Slide 3: Outline
Different visions of the Internet of Things (IoT) paradigm
Enabling technologies, their advantages and disadvantages
IoT Applications

## Slide 4: Impact of IoT
US National Intelligence Council (NIC) lists IoT as one of six ‘‘Disruptive Civil Technologies” giving US the edge in terms of national power
NIC foresees both benefits and threats
  ‘‘by 2025 Internet nodes may reside in everyday things – food packages, furniture, paper documents, and more”.
  ‘‘popular demand combined with technology advances could drive widespread diffusion of an Internet of Things (IoT) that could, like the present Internet, contribute invaluably to economic development”.
  ‘‘to the extent that everyday objects become information security risks, the IoT could distribute those risks far more widely than the Internet has to date”.

## Slide 5: Challenges of IoT
Fully interoperate a large number of heterogeneous interconnected devices, which may
  have low computation and energy capacity
  require resource efficient solutions
  require scalable solutions
Integrates high degree of smartness with adaptation and autonomous-ness
Guarantee trustworthiness with security and privacy

## Slide 6: Views of IoT
Internet oriented
  Interconnect things with standard communication protocols
Things oriented
  Uniquely address things
Semantic oriented
  Represent and store exchanged information

## Slide 7
Internet of Things
“Things”
oriented visions
“Semantic”
oriented visions
“Internet”
oriented visions
Semantic
Technologies
Reasoning over data
Semantic execution environments
IPSO (IP for Smart Objects)
Internet 0 (IP over anything)
Web of Things
Communicating
things
Connectivity for anything
Everyday Objects
uID
Smart Items
WISP
Wireless Sensors and Actuators
Smart Semantic Middleware
Internet of Things from different visions
[1]

## Slide 8: First definition of IoT
Comes from a ‘‘Things oriented” perspective
  Interconnecting simple Radio-Frequency IDentification (RFID) tags
Coined by Auto-ID Labs, which
  Are a world-wide organization of academic research laboratories on networked RFID and emerging sensing technologies.
  Advocate the Electronic Product Code™ (EPC) for broad adoption of RFID in world-wide modern trading networks
  Create the industry-driven global standards for the EPCglobal Network™

## Slide 9: uID
Unique/Universal/Ubiquitous IDentifier (uID) is a competing architecture
  Development of middleware based solutions for globally addressable objects
RFID is the mainstream driving the vision
  RFID is mature, of low cost, and has strong support from the business community

## Slide 10: Future of IoT
Will contain diverse device, network, and service technologies
Driving components linking the real world with the digital world
  Near Field Communications (NFC)
  Wireless Sensor and Actuator Networks (WSAN)
  RFID
Ongoing major projects developing relevant platforms
  WISP (Wireless Identification and Sensing Platforms) project.
Spime, a concept related to IoT, refers to an object
  trackable through space and time throughout its lifetime
  Sustainable
  Enhanceable
  Uniquely identifiable

## Slide 11: the ITU vision of the IoT
ITU (International Telecommunication Union)
‘‘from anytime, anyplace connectivity for anyone, we will now have connectivity for anything”
‘‘Things having identities and virtual personalities operating in smart spaces using intelligent interfaces to connect and communicate within social, environmental, and user contexts”

## Slide 12: Outline
Different visions of the Internet of Things (IoT) paradigm
Enabling technologies, their advantages and disadvantages
IoT Applications

## Slide 13: Enabling technologies
Identification
Sensing
Communication technologies
Middleware

## Slide 14: RFID
Architecture: one or more reader(s) and multiple RFID tags
Tags
  A small microchip1 attached to an antenna, e.g. Hitachi tag 0.4 mm x 0.4 mm x 0.15 mm
  Attached objects (including persons or animals).
  A unique identifier
Readers
  Generate a radio frequency signal to query tags
  Trigger the tag transmission by the emitting signal
  Receive tag IDs.
Properties
  Monitor objects in real-time
  No need of line-of-sight
  Mapping objects into the virtual world
Various applications including logistics, e-health and security.

## Slide 15: Different RFID Based on Power Capability
Passive RFID tags
  No onboard power supplies
  Harvest the energy from the query signal of a RFID to transmit their IDs
Semi-passive RFID tags
  Batteries powered reception
  Reader signal powered transmission
Active RFIDs
  Battery powered reception and transmission
  Highest radio coverage with higher production costs

## Slide 16: Sensor networks
A sensor network
  Sensing nodes communicate in a multi-hop fashion wirelessly.
  Nodes report sensing results to sink nodes.
Design objectives of layers of communication
  Energy efficiency, given energy is scarce
  Scalability for the large number of nodes
  Reliability in data transmission in case of urgent events
  Robustness in case of failures

## Slide 17: IEEE 802.15.4 Sensor Networks
Defines the physical and MAC layers for low-power, slow communications in wireless personal area networks (WPAN)
No specifications on the higher layers of the protocol stack, .e.g. connecting sensor nodes into the Internet.
Challenges for standardizing up-layer protocols
  A very large number of nodes v.s. IP
  802.15.4 physical layer packet is 127 bytes and too small for IP
  Sensor nodes often in a sleep mode for energy saving are anomalous for IP networks.

## Slide 18: Use of Sensor Networks
Integration of sensing technologies into passive RFID tags
  New IoT applications into the IoT context, e.g. e-health
Intel wireless identification and sensing platforms (WISP).
  Powered and read by passive RFID readers (no need of batteries),
  Used to measure quantities such as light, temperature, acceleration, strain, and liquid level.

## Slide 19: Comparison between RFID, wireless sensor networks, and RFID sensor networks
RFID sensor networks (RSN)
  Small, RFID-based sensing and computing nodes
  RFID readers as sink nodes and power source
 | Processing | Sensing | Communication | Range (m) | Power | Lifetime | Size | Standard
RFID | No | No | Asymmetric | 10 | Harvested | Indefinite | Very small | ISO 18000
WSN | Yes | Yes | Peer-to-peer | 100 | Battery | <3 years | Small | IEEE 802.15.4
RSN | Yes | Yes | Asymmetric | 3 | Harvested | Indefinite | Small | None
Table 1 Comparison between RFID systems, wireless sensor networks, and RFID sensor networks.
[1]

## Slide 20: Middleware
A software layer or a set of sub-layers between underlying technological and application levels.
Hiding the details of lower layer technologies
  Exempt programmers from hardware and system details
  Enable programmer to focus on their applications enabled by the infrastructure

## Slide 21: Service Oriented Architecture (SOA)
Decompose complex and monolithic systems into simpler and well-defined components.
  Often not layered structure
Use common interfaces and standard protocols for easy interconnection
Abstract devices functionalities and communications functionalities
  Common set of services
  An environment for service composition

## Slide 22: SOA-based Architecture
Objects
Object
Abstraction
Service
Management
Service
Composition
Applications
Management of Trust, Privacy, Security
Fig.2. SOA-based architecture for the IoT middleware
[1]

## Slide 23: SOA Components
Applications – implementing the (distributed) system’s functionalities by using
  Standard web service protocols
  Service composition technologies
Service composition - Composition of single services for applications
  Services are visible assets
  Use business workflow languages to compose complex services

## Slide 24: SOA Components (Cont’d)
Service management – providing object dynamic discovery, status monitoring, and service configuration
  A service repository lists the catalogue of services and associated objects for easy reference
Object abstraction: standardizing access to different devices through a common language and procedure
  Interface layer – use a web interface exposing the methods; manages communications with the external world.
  The communication sub-layer – implementing the web service methods and communicating with the real-world objects

## Slide 25: SOA Components (Cont’d)
Trust, privacy and security management
  For example, malicious query of RFID tags for surveillance of our lives.
  Managed by the middleware for all the exchanged data.
  Built on one specific layer or distributed through all layers,
  No obvious degradation of system performance

## Slide 26: Other Architectures - Fosstrak
Management of RFID related applications
An open source RFID infrastructure implementing the EPC Network specifications
  Data dissemination, aggregation, filtering, interpretation
  Writing to a tag, trigger RFID reader from external sensors
  fault and configuration management
  Sharing RFID triggered business events, lookup and directory service
  Tag identifier management, and privacy

## Slide 27: Other Architectures - e-SENSE project
Capturing ambient intelligence through WSNs
Four logical subsystems
  Application, management, middleware, and connectivity.
  Each subsystem uses service access points to provide access to other subsystems
This entire stack is implemented in a full function sensor node and a gateway node?
  A reduced-function sensor node has fewer functions.
The middleware subsystem works in a distributed fashion
The result can be sent to an actuating node and/or to the fixed infrastructure through a gateway

## Slide 28: Outline
Different visions of the Internet of Things (IoT) paradigm
Enabling technologies, their advantages and disadvantages
IoT Applications

## Slide 29: Applications and Example Scenarios
Transportation and logistics domain.
Healthcare domain.
Smart environment (home, office, plant) domain.
Personal and social domain
Transportation and logistics
Logistics
Assisted driving
Mobile ticketing
Environment monitoring
Augmented maps
Healthcare
Tracking
Identification authentication
Data collection
Sensing
Smart environments
Comfortable homes/offices
Industrial plants
Smart museum and gym
Personal and social
Social networking
Historical queries
Losses
Thefts
Futuristic
Robot taxi
City information model
Enhanced game room
[1]

## Slide 30: Transportation and Logistics
Logistics: Real-time monitoring of the supply chain, such as raw material purchasing, transportation storage, and after-sales service, for example by use of RFID and NFC
Assisted driving: Collision avoidance, monitoring of transportation of hazardous materials, road traffic patterns
Mobile ticketing: NFC tag
Monitoring environmental parameters: transportation of fruits, fresh-cut produce, meat, and dairy product with monitored environment
Augmented maps: Tagged touristic maps for read by NFC-equipped phones

## Slide 31: Healthcare Domain
Tracking: the identification of moving person or object Identification and authentication: patient identification, electronic medical record maintenance, and infant identification to prevent mismatching
Data collection: automatic form processing, process automation, automated care and procedure auditing, and medical inventory management
Sensing: diagnosing patient conditions, providing real-time information on patient health indicators

## Slide 32: Smart Environments
Comfortable homes and offices
Industrial plants: automation through tagged production parts
Smart museum
  Monitored museum environment good for expositions
Smart gym
  Personalized training with loaded health parameters to prevent overtraining or ensure appropriate exercises.

## Slide 33: Personal and Social
Social networking: RFID tags
Historical queries of where, how, and with whom or what through for example the Google Charts API
Losses: view the last recorded or real-time location of tagged objects
Thefts: similar to the loss

## Slide 34: Futuristic applications domain
Robot taxi: adapt to real-time traffic, reduce congestion reduce congestion of busy roads
City information model: monitoring the status and performance of buildings and urban fabrics – such as pedestrian walkways, cycle paths and heavier infrastructure like sewers, rail lines, and bus corridors
Enhanced game room: body sensor network to sense location, movement, acceleration, humidity, temperature, noise, voice, visual information, heart rate and blood pressure.

## Slide 35: Open Issues
Open issue | Brief description of the cause | Details in
Standards | There are several standardization efforts but they are not integrated in a comprehensive framework | Section 5.1
Mobility support | There are several proposals for object addressing but none for mobility support in the IoT scenario, where scalability and adaptability to heterogeneous technologies represent crucial problems | Section 5.2
Naming | Object Name Servers (ONS) are needed to map a reference to a description of a specific object and the related identifier, and vice versa | Section 5.2
Transport protocol | Existing transport protocols fails in the IoT scenarios since their connection setup and congestion control mechanisms may be useless; furthermore, they require excessive buffering to be implemented in objects | Section 5.2
Traffic characterization and QoS support | The IoT will generate data traffic with patterns that are expected to be significantly different from those observed in the current Internet. Accordingly, it will also be necessary to define new QoS requirements and support schemes | Section 5.2
Authentication | Authentication is difficult in the IoT as it requires appropriate authentication infrastructures that will not be available in IoT scenarios. Furthermore, things have scarce resources when compared to current communication and computing devices. Also man-in-the-middle attack is serious problem | Section 5.3
Data integrity | This is usually ensured by protecting data with passwords. However, the password lengths supported by IoT technologies are in most cases too short to provide strong levels of protection | Section 5.3
Privacy | A lot of private information about a person can be collected without the person being aware. Control on the diffusion of all such information is impossible with current techniques | Section 5.3
Digital forgetting | All the information collected about a person by the IoT may be retained indefinitely as the cost of storage decreases. Also data mining techniques can be used to easily retrieve any information even after several years | Section 5.3
Table 2 Open research issues
[1]

## Slide 36: Standardization activity
Different sections of the Auto-ID Lab scattered all over the world
European Commission and European Standards Organizations (ETSI, CEN, CENELEC, etc.) and international counterparts ISO, ITU
IETF, EPCglobal, etc.
Standard | Objective | Status | Comm. Range(m) | Data rate (kbps) | Unitary cost ($)
EPCglobal | Integration of RFID technology into the electronic product code (EPC) framework, which allows for sharing of information related to products | Advanced | ~ 1 | ~ 10² | ~ 0.01
GRIFS | European Coordinated Action aimed at defining RFID standards supporting the transition from localized RFID applications to the Internet of Things | Ongoing | ~ 1 | ~ 10² | ~ 0.01
M2M | Definition of cost-effective solutions for machine-to-machine (M2M) communications, which should allow the related market to take off | Ongoing | N.S. | N.S. | N.S.
6LoWPAN | Integration of low-power IEEE 802.15.4 devices into IPv6 networks | Ongoing | 10 - 100 | ~ 10² | ~ 1
ROLL | Definition of routing protocols for heterogeneous low-power and lossy networks | Ongoing | N.S. | N.S. | N.S.
NFC | Definition of a set of protocols for low range and bidirectional communications | Advanced | ~ 10² | Up to 424 | ~ 0.1
Wireless Hart | Definition of protocols for self-organizing, self-healing and mesh architectures over IEEE 802.15.4 devices | Advanced | 10 - 100 | ~ 10² | ~ 1
ZigBee | Enabling reliable, cost-effective, low-power, wirelessly networked, monitoring and control products | Advanced | 10 - 100 | ~ 10² | ~ 1
Table 3 Characteristics of the most relevant standardization activities
[1]

## Slide 37: Addressing and Networking Issues
6LoWPA: IPV6 addressing for low-power wireless
  Enough?
Integration of RFID tags through 64–96 bit identifiers by EPCglobal, solutions into IPv6 networks
Open issues:
  Mobility support
  Object Name Service (ONS) like DNS
  Reliable transmission and congestion control: tcp too costly in terms of overhead and buffering?

## Slide 38: Security
Physical attack, eavesdropping, weak security schemes because of poor computation power
  authentication and data integrity
  proxy attack problem, also known as the man-in-the-middle attack
Time
A
B’
A’
B
Time
Time
Time
Query
Message(Query)
Copy of the Query
Reply
Message(Reply)
Copy of the Reply
Man in the middle attack

## Slide 39: Security (Cont’d)
Data integrity to detect the data change
  Unattended RFID systems
  Data modified while stored in the node or during transmission
Typical cryptographic algorithms too costly for low energy and bandwidth IoT nodes

## Slide 40: Privacy
IoT devices are pervasive
Privacy solutions
  individuals control their data in terms of collection by who and when
  Personal data should be used for only authorized services by authorized service providers
  Personal data should be stored only when really needed

## Slide 41: Privacy (Cont’d)
Challenges
  Pervasive sensor networks monitoring individuals entering. How to control?
Solutions
  Privacy broker
  digital forgetting? (delete on purpose automatically)

## Slide 42: References
[1] Luigi Atzori, Antonio Iera, Giacomo Morabito, The Internet of Things: A survey, Computer Networks 54 (2010) 2787–2805
[2] Jayavardhana Gubbia, Rajkumar Buyyab, Slaven Marusic, Marimuthu Palaniswami, Internet of Things (IoT): A vision, architectural elements, and future directions, Future Generation Computer Systems 29 (2013) 1645–1660
[3] Zhen Ling, Junzhou Luo, Yiling Xu, Chao Gao, Kui Wu, Xinwen Fu, "Security Vulnerabilities of Internet of Things: A Case Study of the Smart Plug System", accepted to appear in IEEE Internet of Things Journal (IoT-J), 2017.