## Slide 1: IoT Security and Privacy
Secure Bootstrapping

## Slide 2: Learning Outcomes
Upon completion of this unit:
Student will understand trusted boot
Students will understand secure boot
Students will understand TPM and its usages
Students will understand remote attestation
Students will understand tamper resistant/proof/response hardware and its usage

## Slide 3: Main References
[1] Bryan Parno, Jonathan M. McCune, Adrian Perrig, Bootstrapping Trust in Modern Computers, Springer Publishing Company, Incorporated ©2011
[2] Bryan Parno, Bypassing Local Windows Authentication to Defeat Full Disk Encryption, Black Hat Europe 2015

## Slide 4: Outline
What Do We Need to Know?
Can We Use Platform Information Locally?
Can We Use Platform Information Remotely?
How Do We Make Sense of Platform State?
Roots of Trust
Challenges in Bootstrapping Trust in Secure Hardware
Validating the Process

## Slide 5: A Challenge for System Security
How can you trust a system?

## Slide 6: Bootstrapping Trust
How to convey information about a computer’s current execution environment to an interested party?
  Enable a user to verify that her computer is free of malware or a remote web server will handle her data responsibly (?)
Requires some foundational root of trust
Trusted Computing
  Trusted Platform Module (TPM), deployed on over 350 million computers

## Slide 7: Trust Human v.s. Trust Computer
Trust in a human is often based on identity
Even if a human is trusted, can his computer be trusted?
  Authentication is to authenticate the identity of Alice behind a computer
  Not that Alice’s laptop is free of malware
How do we trust a computer?

## Slide 8: Computer’s State
What is a computer’s current state?
Hardware configuration
  Certification from the computer’s manufacturer
Running code
  How to identify code? It is the code that you expect, not code that has been maliciously changed

## Slide 9: Code Identity
Code identity can be achieved through a cryptographic hash over
  Software
  Inputs
  Libraries
  Configuration files
The calculation of the code identity is often called measurement,
For bootstrapping trust, we need to record at least,
  Identity of the code currently in control of the system.
  Identity of any code that could have affected the security of the currently executing code.

## Slide 10: When and Who Performs Measurements
When to measure a software
  before it starts
Software that starts in the order of S1, S2, …, Si, …, Sn, Sn+1
  Si is running and measures Si+1, before Si+1 starts
  These measurements form chain of trust
Who (or what) measures the first software (S1)
  Who or what measures S1 is the root of trust, for example, hardware-based root of trust .
  Can a running code self identify/measure itself and submit the measurement?
Notes: The best time to measure software is before it execute.
If the software currently in control of the platform is Sn, then the logical entity to measure Sn is the software that was previously in control of the platform, i.e., Sn−1.
  Before executing Sn , Sn−1 must contain code to record a measurement of Sn in its “pristine” state.
  Si responsible for measuring software Si+1 before giving it control of the platform.
  These measurements document the chain of trust
Who (or what) measures the first software (S1) to execute on the system
  Ultimately, measuring code identity requires a hardware-based root of trust .
After all, if we simply ask the running code to self-identify, malicious software will lie.

## Slide 11: Trusted Boot
A hardware-based root of trust initiates the chain of trust
  Measures the initial BIOS code and runs it
BIOS then measures and runs bootloader,
Bootloader measures and runs the operating system (OS).
OS can measure each application
No enforcement of what to do if a measurement is not right
System (P1, C1)
System (Hardware)
System (P2, C2)
Program P1
Configuration C1
Program P2
Configuration C2
Measure
Execute
Measure
Execute
m1
m2
L=L||m2
L=L||m1

## Slide 12: Trusted Boot Secure Boot
L* - an approved list
System (P1, C1)
System (Hardware)
System (P2, C2)
Program P1
Configuration C1
Program P2
Configuration C2
Measure
Execute
Measure
Execute
m1
m2
L=L||m2
L=L||m1
If m1 L*, then HALT
If m2 L*, then HALT

## Slide 13: Secure Measurements in Trusted Boot
What if measurements be erased by malicious software?

## Slide 14: Execution handoffs
P1, C1
Hardware
P2, C2
P1, C1 (e.g. OS)
P2, C2
a. One-way handoff
b. Temporary handoff
Privilege

## Slide 15: Two Attacks against the Transfer
Handoff attack - Trusted software unintentionally executes malicious software
Privilege escalation attack - less privileged code exploits privileged code to
  access secrets of privileged code,
  erase the record of the malicious code’s presence, or
  create fake records of other software.

## Slide 16: Certificate Chains Securing Measurements
Before Pi+1 runs Pi
  Generates a public key pair for Pi+1 - (ei+1, di+1)
  Creates a certificate containing Pi+1 and a measurement mi+1.
  Erases its own secrets di
  Loads the new software, providing the new keypair and certificate as inputs.
The hardware’s public key can be used to verify the certificate chain
Hardware
Program 1
Program 2
(eH, dH)
{ e1,d1 }
Sign(dH, e1||m1)
{e2,d2 }
Sign(d1, e2||m2)

## Slide 17: What Certificate Chains Can Do?
Certificate chains prevent handoff attacks in the trusted boot (not secure boot)
  Trusted boot is necessary since we do not want to halt the system sometimes
  So the question is when the malicious software runs, can it fabricate its certificate?
Notes:   Since by the time malicious code is loaded, the keys used to generate the certificate chain have been erased
  If the keys are not erased, a started malware may create another certificate (e.g. for the original program) and cheat

## Slide 18: What Certificate Chains Can Do? (Cont’d)
A certificate chain cannot prevent a privilege escalation attack
  To maintain the certificate chain, privileged code has to keep its private key
  What if P2 exploits P1 and takes the privilege of P1?
P1, C1 (e.g. OS)
P2, C2
Privilege
Notes: E.g. If the OS erases its secret key before handing control to Application 1, then it will not be able to generate a certificate for applications launched later

## Slide 19: Hash Chain Securing Measurement
Hash chains can be more efficient recording software measurements.
  Only a constant amount of secure memory to record an arbitrarily long, append-only list of code identities.
Hash chain is stored in secure memory can defeat both privilege escalation and handoff attacks
  What if the certificate chain is stored in secure memory? Too large?
Trusted Platform Module (TPM) uses hash chain to store measurements

## Slide 20: How Hash Chain Works?
Hardware-backed hash chain,
  Use protected memory register initialized to a known value (e.g., 0) when the computer first boots.
  A hardware API is used to extend identity of a code, I, into the log
Calculate new hash: V  Hash(V || I)
  I: the identity record of the code and can be saved for later reference
  V: the current register value V
Given collision-resistant hash, V guarantees integrity of the append-only log
Malicious software cannot erase its identity from the log without rebooting the platform and losing control of the machine.

## Slide 21: TPM-Based Measurement Example
BIOS (B), bootloader (L), and operating system (O) should support measurement collection.
  If not, they have to be changed
When the computer first boots, the TPM’s Platform Configuration Registers (PCR) are initialized to a known value (e.g., 0).
ROM code measures BIOS (B), invokes PCRExtend with a valid PCR index, and then runs BIOS
  PCRExtend(5, B) means PCR5  H(0||B)
BIOS measures bootloader, updates PCR, and runs bootloader
  PCRExtend(5, L) : PCR5  H( PCR5||L) = H( H(0||B)||L)
Bootloader will extend a measurement of the OS (O) into the TPM before running OS
Notes: Canonical
conforming to a general rule or acceptable procedure : orthodox His proposals were generally accepted as canonical.

## Slide 22: TPM-Based Measurement Example (Cont’d)
OS extends a measurement of the application (A) into the TPM and runs the application.
  As a result, PCR5 <= h = H(H(H(H(0||B)||L)||O)||A )
  Notice that the entire boot sequence is captured in a single hash value.

## Slide 23: Recording Dynamic Properties
Is measuring code identity is sufficient to guarantee security?
What if the system accepts user inputs, which exploit system vulnerabilities?
  Buffer overflow?
In addition to code identity, we also want to know dynamic properties of code
  Integrity of the code’s control flow (e.g. function call)
  Integrity of its data structures (e.g., the stack), or
  Information-flow control.

## Slide 24: Load-time Dynamics Analysis
Transform the program and record identity of transformed program
  Inserting inline reference monitors that enforce a variety of properties, such as stack and control-flow integrity
Recording code identity of the transformed code ensures that a program with the appropriate built-in dynamic property enforcements was loaded and executed.
Load-time dynamics analysis does not protect against attacks that do not tamper with valid control flows.
  For example, a buffer overflow attack might overwrite the Boolean variable isAdministrator to give the attacker unexpected privileges.

## Slide 25: Run-time Dynamics Analysis
A trust code (e.g. Java Virtual Machine) dynamically enforces a given security property on less-privileged code.
“semantic” attestation - a language runtime (e.g., the Java or .NET virtual machine) monitors and records information about the programs it runs.
  Information includes the class hierarchy or a particular security policy.

## Slide 26: Which Property is Necessary?
Many code properties are relevant to security
Which one is fundamentally needed?
  Many dynamic properties can be achieved via code identity
  The identity of the code conveys the expected dynamic properties
  Or dynamic properties enforced on other pieces of software
Other properties may not be that fundamental
Additional hardware support for monitoring (or enforcing) dynamic properties are also necessary
  Code identity should be implemented as a higher priority
Notes: The converse is not true (i.e. other properties may not be that fundamental)
  The currently running code respected its intended control flow, then it is not clear how to use that mechanism to provide code identity
  A malicious program may happily follow its intended control-flow as it conveys the user’s data to an attacker
  Knowing that a particular invariant has been maintained, whether it is stack integrity or information-flow control, is not particularly useful without knowing more about the context (that is the code) in which the property is being enforced

## Slide 27: Outline
What Do We Need to Know?
Can We Use Platform Information Locally?
Can We Use Platform Information Remotely?
How Do We Make Sense of Platform State?
Roots of Trust
Challenges in Bootstrapping Trust in Secure Hardware
Validating the Process

## Slide 28: Secure Boot
Measurement of next code to run is compared against a list of measurements for authorized software
  Authorized software - signed software by a CA
  Where to save CA’s certificate? Firmware? Can be saved anywhere since it is just a certificate?
Secure boot halts the boot process if unauthorized code is detected
Example system - AEGIS.
  Measure next code to run, check its identity against a certificate from the platform’s owner.
  The certificate identifies authorized software.
  No certificate, no running

## Slide 29: Storage Access Control Based on Code Identity
How to protect the secrets that applications generate for a long term? Examples secrets include
  keys used for full disk encryption or email signatures, and
  a list of stored passwords for a web browser.
Solution: access control mechanism to protect cryptographic keys
  where access policies consist of sets of allowed platform configurations
  only if the policy is met, access is granted

## Slide 30: IBM 4758 – Secure Storage
IBM 4758 family of cryptographic co-processors
  Tamper-responding storage in battery-backed RAM (BBRAM).
  Additional flash memory encrypted with keys maintained in BBRAM.
Physical tampering with the device will result in it actively erasing secrets.
Root cryptographic keys for protected storage can be kept in BBRAM

## Slide 31: IBM 4758 Storage Access Restrictions
Storage access restrictions based on the concept of software privilege layers.
  Layer 0: read-only firmware.
  Layer 1: the IBM-provided CP/Q++ OS by default.
  Layers 2 and 3: applications.
Each layer can store secrets either in BBRAM or in flash.
A hardware ratcheting lock prevents a lower privilege layer from accessing the state of a higher-privilege layer.
  Secrets of layer 1 cannot be accessed by applications at layer 2 or 3
Notes: Extensions to the OS in layer 1 could permit arbitrarily sophisticated protected storage properties
  for example, an extension could provide a sealed storage facility (similar to the TPM functionality discussed below) for binding secrets to a particular software configuration.
The BBRAM is also ideal for storing secure counters, greatly simplifying defense against state replay attacks.

## Slide 32: TPM-Based Sealed Storage
Software on the platform’s main CPU seals or binds secrets to a set of measurements representing some future platform state
Both operations (seal and bind) essentially encrypt the secret value provided by the software.
TPM will refuse to perform a decryption, unless the current values in its Platform Configuration Registers (PCR) match those specified during the seal or bind operation.

## Slide 33: Full disk encryption
The disk encryption keys can be sealed to measurements representing the user’s operating system (Specific OS, disk encryption keys)
  e.g. Microsoft BitLocker does it [2]
  The disk can only be decrypted if the intended OS kernel has booted?
Connecting disk encryption with code identity ensures that
  Boot sequence cannot be changed to load malware or other OS
Seal and bind operations use 2048-bit asymmetric RSA keys
  RSA keys are generated on TPM
  Private keys are never released in the clear.
  Encryption scheme provides both secrecy and integrity

## Slide 34: Simplified BitLocker boot process
TPM
BIOS/EFI
MBR/BOOT LOADER
Operating System
(Encrypted)
RAM
1.1: Read and hash
1.2: Save to PCRs
2.1: Unseal key after verification
1.3: Pass control
2.3: Pass control
2.2: Save key to RAM
3: Use key as needed
Data flow
Control flow
Legend
Notes: 1. The BIOS/EFI hashes the next boot stage: the MBR, bootloader, etc. It puts the result in TPM
PCRs. Control is passed to the next boot stage.
2. The Windows bootloader asks the TPM to unseal the BitLocker encryption key, which will verify
the current PCR values. The returned key is stored in RAM, the operating system is decrypted, and
control is passed to the operating system.
3. The operating system continues to decrypt disk contents on the y using the key stored in RAM.

## Slide 35: TPM Key Hierarchy
Because of limited storage space, TPM uses a key hierarchy to protect storage keys.
  Private portion of its Storage Root Keypair saved in TPM’s protected storage.
  Public portion of the Storage Root Keypair to encrypt private portion of other keys
  Computer software manages encrypted keys used for seal and bind operations
Before performing a seal/bind operation,
  The software loads encrypted keys into TPM.
  TPM decrypts the ciphertext to obtain a key, checks its integrity, and then uses it to perform the seal/bind operation.
Notes: Before performing a seal/bind operation,
  The software (OS or VMM) loads encrypted keys into TPM.
  TPM decrypts the ciphertext to obtain a key, checks its integrity, and then uses it to perform the seal/bind operation.
In this way, the TPM supports an arbitrary number of storage keys while using only a constant amount of protected storage.
  Software can generate symmetric keys and use the TPM to protect the symmetric keys.

## Slide 36: TPM Key Hierarchy (Cont’d)
Benefits of TPM key hierarchy
  Arbitrary number of storage keys
  Constant amount of protected storage.
Software can generate symmetric keys and use the TPM to protect the symmetric keys.
Notes: Before performing a seal/bind operation,
  The software (OS or VMM) loads encrypted keys into TPM.
  TPM decrypts the ciphertext to obtain a key, checks its integrity, and then uses it to perform the seal/bind operation.
In this way, the TPM supports an arbitrary number of storage keys while using only a constant amount of protected storage.
  Software can generate symmetric keys and use the TPM to protect the symmetric keys.

## Slide 37: Sealing Data
Seal operation inside TPM: (encrypting a secret value, setting access policy)
  Access policy: controls the decryption of encrypted secret.
  Access policy format: a set of PCR indices and the right values for decryption;
  PCR values in the access policy may be different from the current PCR values.
Unseal - when software wishes to decrypt the sealed secret in the future, it asks the TPM to unseal it.
  TPM decrypts the ciphertext internally;
  If access policy is met, the TPM releases the plaintext

## Slide 38: Example of Sealing Data: Secure software updates
Trusted software module P decides to upgrade to a new version P’.
  P has secret data that P’ should inherit.
  How can P give the secret data to P’?
P validates the upgrade e.g. through digital signature
P passes that data to a seal operation, specifying PCR values corresponding to P’.
When P’ runs, P’ asks TPM to unseal the data
  How? Hint: refer to the definition of unsealing

## Slide 39: Binding Data
Binding – Encrypt data with a public binding key, which is derived from a storage key
  Encryption need not take place on the TPM.
  Flexible when performing data encryption because there is too much data
Encrypted data is bound to the specific public binding key
  Not bound to TPM
For example
  An AES key is bound to a public binding key
  The AES can be used to encrypt large data
Notes: but it means that the resulting ciphertext does not include a record of the entity that originally invoked the bind operation.
However, because the private key used for unbinding data can be locked to PCR values, an entity in possession of an authentic public binding key can encrypt data (e.g., a cryptographic challenge such as a nonce) using a binding key, and hence learn something about the software state of the platform that performed the unbind operation.

## Slide 40: TPM-Based Sealed Storage Example
Goal: Only application A can access its secret
BIOS (B), bootloader (L) and the operating system (O)
  Support TPM.
Application (A) is running and PCR5 is :
  h = H(H(H(H(0||B)||L)||O)||A)
A can generate secret data Dsecret and seal it under the current value of PCR5 by invoking:
  Seal( (5), Dsecret)  C = EncK((5,h)||Dsecret )
  where K is a storage key generated by the TPM.
C is returned to the software that invoked the seal operation.
If the same boot sequence occurs later, A can unseal the secret
  Otherwise, no

## Slide 41: Outline
What Do We Need to Know?
Can We Use Platform Information Locally?
Can We Use Platform Information Remotely?
How Do We Make Sense of Platform State?
Roots of Trust
Challenges in Bootstrapping Trust in Secure Hardware
Validating the Process

## Slide 42: Attestation
Attestation - conveying measurement chains to an external entity in an authentic manner, called outbound authentication too
  A remote party (verifier) would like to learn the security status of a local system (attestor)
Verifier needs an authentic measurement chain represents the software state of attestor
  A verifier’s trust in an attestor’s measurement chain builds from a hardware root of trust.
Prerequisites for attestation: the verifier
  understands the attestor’s hardware configuration and
  has an authentic public key bound to the hardware root of trust.

## Slide 43: General Purpose Coprocessor-Based Attestation
A coprocessor is a computer processor used to supplement the functions of the primary processor (the CPU).
  General-purpose cryptographic co-processors
Coprocessor applications authenticate themselves to remote parties
  Generate and maintain authenticated key pairs
  Communicate securely with remote party.
  Keep a private key in tamper-protected memory
  Have certificates signed by CA

## Slide 44: TPM-Based Attestation
Less flexible than general coprocessor-based attestation, without general-purpose computation.
For attestation, attestor’s software relays information between the remote verifier and the TPM
Attestor’s TPM has generated an Attestation Identity Keypair (AIK),
  An asymmetric keypair
  Public key known to the verifier in advance, and
  Private on the TPM.

## Slide 45: TPM-Based Attestation Protocol
The verifier sends a nonce to the attestor
  Prevent replay of old attestations
The attestor asks the TPM to generate a Quote.
  Quote: digital signature(verifier’s nonce, the current measurement in the TPM’s Platform Configuration Registers (PCRs)).
The attestor sends both the quote and an accumulated measurement list to the verifier. This measurement list
  Contains enough information about measured entities so that the verifier will know what are being measured.
  Implementation-specific, e.g. the hash and full path to a loaded executable
To verify the measurement list, the verifier performs basically signature verification
Notes: To verify the measurement list, the verifier
  Computes the hash aggregate supposedly generated by the measurement list
  Compares it to the aggregate signed by the TPM Quote.

## Slide 46: TPM-Based Attestation Protocol
TPM
PCR 0
…
PCR N
Attestation service
Daemon
Measurement List
Program 1, Configuration 1
Program 1, Configuration 1
…
External verifier
1. AttRequest
2. QuoteRequest
3. QuoteResponse
4. Retrieve
5. QuoteResponse, measurement list
6. Validate response

## Slide 47: Outline
What Do We Need to Know?
Can We Use Platform Information Locally?
Can We Use Platform Information Remotely?
How Do We Make Sense of Platform State?
Roots of Trust
Challenges in Bootstrapping Trust in Secure Hardware
Validating the Process

## Slide 48: Coping With Information Overload
Can we build perfect secure software?
  If yes, a computer running such software can be trusted.
  Unfortunately, no.
Most computers run buggy and unverified code.
State-space explosion
  So many versions, libraries, drivers, dependable applications
How to deal with state-space explosion?
Notes: developing software with strong security properties, even minimal security kernels with limited functionality, has proven to be a daunting and labor-intensive task [5, 73, 101, 107].
As a result, most computers run a large collection of buggy, unverified code.
Worse, both OS and application code changes rapidly over time, making it difficult to decide whether a particular version of software, combined with dozens of other applications, libraries, drivers, etc., really constitutes a secure system.
How to cope with this state-space explosion?

## Slide 49: Focusing on Security-Relevant Code
Only record the identity of code that will affect security.
Reduce the amount of security-relevant code
  Simplifies the verifier’s workload for attestation too
To achieve this reduction, the platform must support multiple privilege layers, preventing privilege-escalation attacks
  The more-privileged code enforces isolation between itself and less-privileged code modules.
  Layering simplifies or interprets information given to a verifer

## Slide 50: Privilege Layering via the Operating System
Marchesini et al. introduce privilege layering OS
A long-term core (an SELinux kernel in their case)
  loads and verifies a policy file supplied by an administrator.
An Enforcer module in the core ensures that only applications matching the policy can execute.
  Kind of the secure boot model.
  Secrets bound to the long-term core, not applications
Remote attestation by verifier
  The long-term core is trustworthy,
  Enforcer is configured with an appropriate policy (i.e., one that satisfies the external party’s requirements).

## Slide 51: Privilege Layering via Virtualization
Microsoft’s Next-Generation Secure Computing Base (NGSCB)
  Security-sensitive operations confined to one virtual machine (VM)
  General purpose computing in another VM
  Virtual machine monitor (VMM), i.e., hypervisor, provides strong isolation between VMs
Remote attestation to verifier
  The identity of the VMM
  A particular VM, rather than applications in the other VMs.
Challenge: privilege-escalation attacks
The impact of NGSCB architecture
  TPM
  DRTM (dynamic root of trust for measurement)
  How to build secure applications on a bootstrapped foundation of trust

## Slide 52: Hardware-Supported Isolation: System-Management Mode
Azab et al. uses System-Management Mode (SMM) to monitor and attest to the integrity of a hypervisor
  No need of software “underneath” the hypervisor.
SMM: a special x86 execution mode invoked via System-Management Interrupts (SMIs) – hardware based
  Often used to control fan speed
  React to special keys on laptop keyboards such as the volume control buttons
Code in an SMI handler operates independently of normal system code, such as the OS or hypervisor
  Can introspect on CPU state and the contents of memory.

## Slide 53: Hardware-Supported Isolation: Dynamic Root of Trust for Measurement
VMM-based isolation includes a lot of non-security-relevant code,
  BIOS, the boot loader, and various option ROMs.
To address these shortcomings, AMD and Intel extended the x86 instruction set to support a dynamic root of trust for measurement (DRTM – also known as late launch ) operation
  Secure Virtual Machine (SVM) by AMD
  Trusted eXecution Technology (TXT) (LaGrande Technology) by Intel
A DRTM operation
  Resets the CPU and memory controller to a known state
  Atomically measures a piece of code into the TPM
  Begins executing the code in a hardware-protected environment.

## Slide 54: Slicing and Privilege Separation
A persistent challenge: most software was written without meticulous attention to the principle of least privilege.
Solution: privilege separation to a legacy codebase, via tools such as PrivTrans
PrivTrans leverages programmer annotations to automatically separate an existing program into privileged and unprivileged components.
The authors compare their results against the manual privilege separation performed for the OpenSSH utility.

## Slide 55: Conveying Higher-Level Information
Convert the information into a set of higher-level properties that facilitate trust judgements
Convey information about software
  Static methods such as type checking
  Inline reference monitors
  Dynamic methods such as hypervisors
  Security kernels
  Language runtimes
Attesting to code identity assures verifier the transformed code runs

## Slide 56: Outsourcing
Outsource the problem of interpreting code identity to a third party.
One strategy
  Clients obtain certificates from their software providers that map hash values to software names and/or versions.
  A client sends these certificates for their attestation
Benefit
  No need of database for mapping hash values to software packages at verifier

## Slide 57: Outline
What Do We Need to Know?
Can We Use Platform Information Locally?
Can We Use Platform Information Remotely?
How Do We Make Sense of Platform State?
Roots of Trust
Challenges in Bootstrapping Trust in Secure Hardware
Validating the Process

## Slide 58: Different Roots of Trust
Trust in any system needs
  a foundation or
  a root of trust
The root of trust can be built upon
  Secret private key embedded in hardware;
  Corresponding public key certified by the hardware’s manufacturer.
  The first piece of code that make measurements (e.g. code in the early boot process)
  Physical hardware itself.

## Slide 59: General-Purpose Tamper-Resistant and Tamper-Responding Devices
Manufacturing tamper-resistant devices is expensive
  No much commercial success
Commercial solutions do use research ideas
  Hardware stores a secret private key,
  Manufacturer digitally signs a certificate of the corresponding public key.
  The verifier uses the certificate to establish trust in the platform.

## Slide 60: Commercial Solutions - Cryptographic co-processors
General-purpose cryptographic co-processors such as IBM PCI-based 4758
  Tamper resistant and tamper-responding properties
Packaging for resisting and responding to physical penetration and fluctuations in power and temperature.
Batteries powering active response to detected tampering
  Immediately erasing internal secrets
  Permanently disabling the device

## Slide 61: Commercial Solutions – Smart Card
Many higher-end smart cards and SIM cards can fight against physical attack, e.g. Infineon line of SLE88 chips
  Sensors to detect voltage fluctuations, glitches, and light,
  Filters designed to smooth power usage and resist power analysis
How it works?
  A private key for authentication is stored in the microprocessor,
  All private key operations within the microprocessor
  The card can interact with untrusted terminals without leaking the key
Low-end smart cards and SIM cards may not have any active tamper response mechanisms, but hardware obfuscation

## Slide 62: General-Purpose Devices Without Dedicated Physical Defenses
Goal: increase the software security of software systems without explicit physical defense measures.
  Achieve different degrees of resilience to physical compromise.
Different physical attacks
  on a daughter card that can be readily unplugged and interposed on,
  soldered to the motherboard,
  integrated with the “super-IO” chip, and
  on the same silicon as the main CPU cores.
Example commodity platforms today
  Trusted Platform Module (TPM), or its mobile counterpart
  Mobile Trusted Module (MTM), or
  a smart card.

## Slide 63: TPM-equipped Platforms
The TPM chip is a hardware device
  No specific tamper resistance.
Trust in the TPM stems from three roots of trust, for Storage, Reporting, and Measurement.
  Trusted storage by an encryption key in TPM’s nonvolatile RAM.
  The root for reporting (remote attestation) by the TPM’s storage facilities.
  TPM measurement by firmware called the Core Root of Trust for Measurement, which initializes the TPM when the system boots.

## Slide 64: MTM-equipped Platforms
The TCG Mobile Phone Working Group (MPWG) has specified a Mobile Trusted Module (MTM)
The MTM specification interleaves two different profiles, depending on the device’s owner: a Mobile Local Owner Trusted Module (MLTM) and a Mobile Remote Owner Trusted Module (MRTM).
  The local owner has physical control over the device, i.e., its user.
  The remote owner is a stakeholder without physical access to the deployed device, e.g., a device manufacturer or a network service provider.
The root of trust for execution typically makes use of the isolated execution features of the platform’s main CPU, e.g., ARM Trust- Zone or TI M-Shield
Boot integrity is provided using a secure boot model.

## Slide 65: Special-Purpose Minimal Devices
Specifically designed for some applications,
What functionality is needed in secure hardware for various classes of applications?
  An open area of research.

## Slide 66: Research Solutions Without Hardware Support
Software-based attestation
Code computes a checksum over itself
A verifier checks the checksum for integrity and also measures the computation time.
  Adversarial interference with the checksum computation will either slow the computation (detectable by the verifier) or will result in an incorrect checksum.
Many other schemes …

## Slide 67: Outline
What Do We Need to Know?
Can We Use Platform Information Locally?
Can We Use Platform Information Remotely?
How Do We Make Sense of Platform State?
Roots of Trust
Challenges in Bootstrapping Trust in Secure Hardware
Validating the Process

## Slide 68: What we have learned so far?
How to use secure hardware mechanisms for secure bootstrap
  Secure hardware to monitor and report on the software state
We can then decide whether to trust the platform
  And what to do else
Secure hardware such as cryptographic co-processors with tamper resistant/proof/response properties is expensive
  Cheaper TPM is sued and against software attacks
  TPM can be defeated by an adversary who possesses it
  TPM can be used for secure boot, measurements and remote attestation
  Recent CPU advances such SGX make measurements simpler

## Slide 69: Remaining Question
How do we bootstrap trust in the TPM itself?
How can a user get the TPM’s public key?
  An authentic public key is needed to verify if we are communicating with the right TPM
Otherwise, cuckoo attack
  Malware on the local machine forwards the user’s messages to a remote adversarial TPM

## Slide 70: Cuckoo Attack
TPML
Verifier
TPMM
Local PC
Remote PC
The case that Verifier does not have the correct public key of TPML

## Slide 71: Potential Solutions
How to securely deliver the TPM’s public key in case of malware attacks?

## Slide 72: Potential Solutions - Establishing a Secure Channel
Hardware-Based Secure Channels
  Special-Purpose Interface. Add a new hardware interface on a computer for an external device to talk directly to the TPM of the computer.
  Existing Interface. Use an existing external interface (such as Firewire or USB) to talk directly to the TPM.
  External Late Launch Data. New CPU features from AMD and Intel.
  Special-Purpose Button that can execute an authenticated code module establishing a secure channel between the verifier (connected via USB, for example) and the TPM

## Slide 73: Cryptographic Secure Channels
Camera-based Channel. Seeing-is-Believing (SiB), an approach - a hash of the platform’s identity can be put in a 2-D barcode on the platform’s case.
Human-based Channel. The hash as an alpha-numeric string that can be entered into a smartphone, or into a dedicated trusted device.
Trusted BIOS outputs the platform’s identity (either visually or via an external interface, such as USB).
Trusted Third Party. A certificate the TPM with a particular machine.

## Slide 74: Outline
What Do We Need to Know?
Can We Use Platform Information Locally?
Can We Use Platform Information Remotely?
How Do We Make Sense of Platform State?
Roots of Trust
Challenges in Bootstrapping Trust in Secure Hardware
Validating the Process

## Slide 75: Validating
How to validate involved hardware, software, and protocols?
From a hardware perspective, Smith and Austel
  discuss efforts to apply formal methods to the design of secure coprocessors
  state formal security goals for such processors.
Bruschi et al. use a model checker to
  find a replay attack in the TPM’s Object Independent Authorization Protocol (OIAP)
  propose a countermeasure to address their attack, though it requires a TPM design change.
Etc.

## Slide 76: References
[1] Bryan Parno, Jonathan M. McCune, Adrian Perrig, Bootstrapping Trust in Modern Computers, Springer Publishing Company, Incorporated ©2011
[2] Bryan Parno, Bypassing Local Windows Authentication to Defeat Full Disk Encryption, Black Hat Europe 2015
[3] Secure the Windows 10 boot process, 06/23/2017

## Slide 77: Backup

## Slide 78: Employing NVRAM
The TPM also includes a limited amount of nonvolatile RAM (NVRAM) that can be used to perform a function similar to sealed storage.
In particular, reading and writing to NVRAM can be restricted based on the contents of the PCRs,
  so an NVRAM location can be made accessible only to a particular collection of software.
Since an NVRAM location can store arbitrary data, the most straightforward approach to “sealing” data is to define an NVRAM location large enough to hold a symmetric key and use the PCR-based restrictions to prevent other software from reading or writing the key.
  The symmetric key can then be used to encrypt and MAC bulk data.

## Slide 79: limitations when using NVRAM
First, software that does not match the PCR restrictions on an NVRAM location may still be able to delete the information stored in that location.
  For example, the TPM owner can both delete and re-establish NVRAM locations.
  Thus, application developers must be cautious when using this facility. In particular, code reading or writing an NVRAM location should verify that the target location has the expected PCR-based restrictions in place.
Second, the v1.2 TPM specification only requires 1,280 bytes of NVRAM, some of which is dedicated to various system features

## Slide 80: Limitations when using NVRAM (Cont’d)
Although reading NVRAM is relatively fast (9.8–14.8 ms) compared to other TPM operations, writing is 3–6x slower (33.9–82.4 ms).
Finally, the NVRAM is only expected to tolerate a limited number (100,000) of write cycles during its lifetime.
  Writing to NVRAM once every second would exhaust its write cycles in less than 28 hours.

## Slide 81: Configuration Changes
An entity may go through one or more upgrades, and it may depend on lower layer software that may also be subject to upgrades.
Thus, preserving desired security properties for code and data (e.g., integrity, authenticity, and secrecy) may depend not only on the versions of software currently running on the coprocessor, but also on past and even future versions.

## Slide 82: Configuration Changes (Cont’d)
The IBM 4758 exposes these notions as configurations and epochs, where configuration changes are secret-preserving and epoch changes wipe all secrets from the device.
During a configuration change, certificate chains incorporating historical data are maintained.
  For example, the chain may contain a certificate stating the version of the lowest layer software that originally shipped on the device, along with a certificate for each incremental upgrade.
  When a remote party interacts with such a device, all information is available about the software and data contained within.
  TPM-based attestations are based on hash chains for at most one boot cycle and does not maintain historic data automatically

## Slide 83: TPM-Based Attestation Protocol (Cont’d)

## Slide 84: Research Projects
μABYSS [221] and Citadel [223] are predecessors of the modern IBM designs, placing a CPU, DRAM, flash ROM, and battery-backed RAM (BBRAM) within a physically tamper-resistant package.
Lee et al. propose the Secret Protected (SP) architecture for virtual secure coprocessing [117 ].
  SP proposes hardware additions to standard CPUs in the form of a small key store, encryption capabilities at the cache-memory interface, new instructions, and platform changes to support a minimalistic trusted path.